## Slide 1: Verilog 2 - Design Examples
Modified by Michael Taylor from Arvind’s MIT 6.375 slides.

## Slide 2: Verilog can be used at several levels
automatic tools to synthesize a low-level gate-level model
High-Level Behavioral
Register Transfer Level
Gate Level
A common approach is to use C/C++ for initial behavioral modeling, and for building test rigs

## Slide 3: Writing synthesizable Verilog Recap: Combinational logic
Use continuous assignments (assign)
  assign c_i = b_o + 1;
Use always_comb blocks with blocking assignments (=)
always_comb
begin
out = 2’d0;
if (in1 == 1)
out = 2’d1;
else if (in2 == 1)
out = 2’d2;
end
Every variable should have a default value to avoid inadvertent introduction of latches
Don’t assign to same variable from more than one always_comb block. Race conditions in behavioral sim, synthesizes incorrectly.
always blocks allow more expressive control structures, though not all will synthesize
default value

## Slide 4: Writing synthesizable Verilog: Sequential logic
Use always_ff @(posedge clk) only with non-blocking assignment operator (<=)
always_ff @( posedge clk )
c_o <= c_i;
Use only positive-edge triggered flip-flops for state
Do not assign the same variable from more than one always_ff block. Race condition in behavioral simulation; synthesizes incorrectly.
Do not mix blocking and non-blocking assignments
  only use non-blocking assignments (<=) for sequential logic.
  only use block assignments (=) for combinational logic.
Like in software engineering, express your design as a module hierarchy that corresponds to logical boundaries in the design. Also, separate datapath and control (more later).

## Slide 5: An Example: Good Style
logic a_n, b_n, c_n;
logic a_r, b_r, c_r;
always_ff @( posedge clk )
begin
a_r <= a_n;
b_r <= b_n;
c_r <= c_n;
end
assign b_n = a_r + 1;
assign c_n = b_r + 1;
+1
a
+1
b
c
Readable, combinational and sequential logic are separated.
Standard naming: A_r is the output of the register and A_n (or A_n) is the input.

## Slide 6: An Example: Good Style
logic a_n;
logic b_n, c_n;
logic a_r, b_r, c_r;
always_ff @( posedge clk )
begin
a_r <= a_n;
b_r <= b_n;
c_r <= c_n;
end
always_comb
begin
b_n = a_r + 1;
c_n = b_r + 1;
end
+1
a
+1
b
c
Readable, combinational and sequential logic are separated.

## Slide 7: Alternate implementation?
logic a_n, b_n, c_n;
logic a_r, b_r, c_r;
always_ff @( posedge clk )
begin
a_r <= a_n;
b_r <= b_n;
c_r <= c_n;
assign b_n = a_r + 1;
assign c_n = b_r + 1;
end
+1
a
+1
b
c
Syntactically Incorrect.

## Slide 8: An Example: Okay, but less readable?
logic a_n;
logic a_r, b_r, c_r;
always_ff @( posedge clk )
begin
a_r <= a_n;
b_r <= a_r + 1;
c_r <= b_r + 1;
end
+1
a
+1
b
c
Is (b_r == a_n+1) ?
Nope - Why?
a_r <= a_n creates
a register between
a_n and a_r, not a wire.

## Slide 9: Another style – multiple always blocks
logic a_n, b_n, c_n;
logic a_r, b_r, c_r;
always_ff @( posedge clk )
a_r <= a_n;
assign b_n = a_r + 1;
always_ff @( posedge clk )
b_r <= b_n;
assign c_n = b_r + 1;
always_ff @( posedge clk )
c_r <= c_n;
+1
a
+1
b
c
Does it have the same functionality?
It generates the same
underlying circuit.
Yes. But why?

## Slide 10: How about this one?
logic a_n, b_n, c_n;
logic a_r, b_r, c_r;
always @( posedge clk )
begin
a_r = a_n;
b_r = b_n;
c_r = c_n;
end
assign b_n = a_r + 1;
assign c_n = b_r + 1;
+1
a
+1
b
c
Will this synthesize?
 Maybe
Is it correct?
 No; Don’t use “blocking assignments” in @posedge clk
blocks. It creates race conditions. Also, use always_ff instead.

## Slide 11: What does this do? (This is correct but bad code.)
logic b_i, c_i;
logic a_r;
logic sel;
always @( posedge clk )
begin
a_r <= 1’b0;
a_r <= b_i;
if (sel)
a_r <= c_i;
end

## Slide 12: Desugar into separate comb. and seq. logic.
logic b_i, c_i;
logic a_r;
logic sel;
always @( posedge clk )
begin
a_r <= 1’b0; // redundant!
a_r <= b_i;
if (sel)
a_r <= c_i;
end
logic a_n, b_i, c_i;
logic a_r;
logic sel;
always_comb
begin
a_n = a_r; // default;
// rdt. but safe
a_n = b_i;
if (sel)
a_n = c_i;
end
always_ff @( posedge clk )
begin
a_r <= a_n;
end

## Slide 13: What does this do? For each always_comb, assign, always_ff statement, draw the gates and wires.
logic a_n, b_i, c_i;
logic a_r;
logic choose;
always_comb
begin
a_n = a_r; // default
a_n = b_i;
if (choose)
a_n = c_i;
end
always_ff @( posedge clk )
begin
a_r <= a_n;
end
b_i
c_i
choose
0
1
a_n
a_r
a_n

## Slide 14: Verilog execution semantics
Confusing
Best solution is to write synthesizable verilog that corresponds exactly to logic you have already designed on paper. Separate combinational from sequential logic.
Debugging is very difficult for Verilog. Don’t write code
and “see if it works.” Test each “unknown” thing individually until you know what it does; then combine into larger entities.
Before you try to simulate, manually check every wire to make sure that it is correctly (1) defined, connected to (2) source and (3) destination, and that (4) the logic driving it appears to be correct.
  This is way faster than finding the same bugs in the waveform viewer!

## Slide 15: SystemVerilog struct example lab 2a examined this
typedef struct packed {
logic [17-1:0] instr;
logic [10-1:0] addr;
} instr_packet_s;
instr_packet_s ip_n, ip_A_r, ip_B_r, ip_C_r;
assign ip_n = ‘{addr: addr_i
, instr: instr_i};
assign { addr_o, instr_o }
= { ip_C_r.addr, ip_C_r.instr };
always_ff @( posedge clk )
begin
{ ip_A_r, ip_B_r, ip_C_r } <=
{ ip_n, ip_A_r, ip_B_r };
end

## Slide 16: Helpful SV Primitives
$bits( ) - number of bits required to hold value:
logic[31:0] foo; // $bits(foo) = 32
struct happy foo; // $bits(struct happy) =
$clog2( ) - number of address bits for a memory of size
- ceiling of log base 2 of X (eg for RF impl.)
// $clog2(1) = 0? = $clog2(2) = 1,
// $clog2(3,4) = 2, $clog2(5,6,7,8) = 3, …
’1,’0,’X,’Z – all 1’s, all 0’s, all X’s, etc.
logic [63:0] word; logic [3:0] byte;
word[byte*8 +: 8] ; start at byte*8; grab 8 bits upwards
word[byte*8 –: 8]; start at byte*8; grab 8 bits downwards

## Slide 17: Helpful SV Primitives, Cont.
typedef enum [2:0] { eFetch, eDecode, eExecute, eMemory, eWriteback } state_e;
state_e substate_r, substate_next;
always_ff @(posedge clk)
substate_r <= reset ? eFetch : substate_next;
always_comb
unique case (substate_r)
eFetch: substate_next = eDecode;
eDecode: substate_next = eExecute;
eExecute:
unique casez (instr_reg)
`SW: `LW: substate_next = eMemory;
default: substate_next = eWriteback;
endcase
eMemory:
unique casez(instruction)
`LW: substate_next = eWriteback;
default: substate_next = eFetch;
endcase
eWriteback: substate_next = eFetch;
default: substate_next = eFetch;
endcase

## Slide 18: Useful functions
instr_packet_s storage [(2**LG_DEPTH)-1:0];
2**LG_DEPTH == 2^LG_DEPTH
Useful for Parameters
when you need a width and also the number of bits to
address that width. Can also use clog2, but that does
not force the user to make things a power of 2.
(| c) // all of the bits of C or’d together (“or reduce”)
(& c) // all of the bits of C and’d together (“and reduce”)
(^ c) // all of the bits of C xor’d together (“xor reduce”)