## Slide 1: Backend Control Logic Design the MBT way
Shown here for a simple MIPS-like design.
Your design has a few differences; for instance it has stalls/restarts from the front end, has memory stalls, different ISA, etc, etc.
Further pipelining of your backend (beyond the 2-way front-end/back-end split) is possible – but get the basic non-pipelined backend working first.

## Slide 2: Recap: The Processor Design Algorithm
Once you have an ISA…
Design/Draw the datapath
  Identify and instantiate the hardware for your architectural state
  Foreach instruction
    Simulate the instruction
    Add and connect the datapath elements it requires
    Is it workable? If not, fix it.
Design the control (single-cycle machine)
  Foreach instruction
    Simulate the instruction
    What control lines do you need?
    How will you compute their value?
    Modify control accordingly
    Is it workable? If not, fix it.

## Slide 3: Derive datapath
(You would create this on a blackboard or whiteboard and powerpoint it up.)

## Slide 4: Define and Name Control Signals
Signal | == 0 | == 1
RegDst | Write to rd | Write to rt
RegWrite | Register writes suppressed | Register writes occur
ALUSrc | 2nd ALU input is R[rd] | 2nd ALU input is the immediate
ALUop | Multiple bits; value determines the operation the ALU will perform. | 
This is control, not datapath

## Slide 5: Define and Name Control Signals
Signal | == 0 | == 1
PCSrc | PC <= PC + 4 | PC <= PC + 4 + immediate
MemRead | Do not read data memory | Perform read at address
MemWrite | Do not write data memory | Perform write at address
MemtoReg | Present ALU result to register file for write | Present ALU result to register file for write.

## Slide 6
`define LW 32'b100011_?????_?????_?????_?????_??????
`define SW 32'b101011_?????_?????_?????_?????_??????
`define ADDIU 32'b001001_?????_?????_?????_?????_??????
`define BNE 32'b000101_?????_?????_?????_?????_??????
reg writes_rf_c; // aka RegWrite;
always_comb
unique casez (IR)
`LW: writes_rf_c = 1’b1;
‘SW: writes_rf_c = 1’b0;
`BNE: writes_rf_c = 1’b0;
`ADDIU: writes_rf_c = 1’b1;
…
default: writes_rf_c = 1’b0;
endcase
reg writes_dmem_c; // aka MemWrite;
always_comb
unique casez (IR)
‘SW: writes_dmem_c = 1’b1;
…
default: writes_dmem_c = 1b’0;
endcase
Writing Control Logic
- hard part is to not make careless mistakes
- important to structure the code to avoid mistakes
Useful Discipline: Always give a default: for unique casez, even if it is empty.
(This enables pass-thru of settings prior to the casez statement; otherwise synthesizer will assume it’s don’t care. )

## Slide 7: Single-Cycle Pipeline Is Often Not Ideal
Your data memory, and possibly other structures can only be read on the clock edge: thus, you need at least two cycles, one for fetch, and another for doing loads.
Instructions may require multiple states – perhaps they read the RAM multiple times, or require too many RF ports
Your design needs to respect the refuse signal, which may affect things.
Long cycle time. Timing Analyzer will identify excessively long paths. Increase clock rate by breaking paths up with registers and adding states. To improve performance, have instructions skip states they don’t need.

## Slide 8: Solution: Convert to Multicycle Data Path
Update your datapath with new registers, as needed.
Draw Finite State Machine
Mentally simulate on your datapath to ensure correctness. Do you wait enough cycles in your state machine such that all inputs have arrived at each datapath element?
Code Enum to define states
Use always_ff to create state registers.
Code next state logic.
Code Logic that determines control signals at each state
    many signals, like muxes, stay steady through all states in the instruction
      unless you reuse a resource more than once in an instruction’s execution
    write enable signals usually are state dependent – if you write too earlier, you will corrupt state that current instruction needs – usually wait until last cycle
    read enables are often state dependent to save power.

## Slide 9: Insert Necessary or Existant Registers
pc_en
dmem_ren
dmem_wen
rf_wen
imem_ren
pc_sel
rf_wr_sel

## Slide 10: Insert Necessary or Existant Registers
pc_en
IR_en
dmem_ren
dmem_wen
rf_wen
pc_sel
dest_sel
imem_ren
rf_wr_sel

## Slide 11: Identify Write/Read Enables
pc_en
IR_en
dmem_ren
dmem_wen
rf_wen
pc_sel
dest_sel
imem_ren
rf_wr_sel

## Slide 12: For each instruction’s datapath components, identify longest latency (in cycles) inputs. This is the cycle it “fires” on.
pc_en
NewPC
Fetch
Execute
Memory
0
1
2
3
IR_en
dmem_ren
dmem_wen
rf_wen
pc_sel
rf_wr_sel
dest_sel
imem_ren

## Slide 13: Then, code up datapath in structural verilog … and move onto control.

## Slide 14: Draw / Debug State machine
NewPC
Fetch
Execute
Memory
~(LW)
LW
pc_en = 1
rf_wen = writes_rf_c;
if (writes_dmem_c)
dmem_wen=1
pc_en = 1
rf_wen=writes_rf_c
imem_ren=1
IR_en=1
dmem_ren=1

## Slide 15: Coding Control: Next State Logic (with a little Synthesizable SystemVerilog; remember macros for LW etc from earlier)
always_ff @(posedge clk)
substate_r <= reset ? sNewPC : substate_n;
always_comb
unique case (substate_r)
sNewPC: substate_n = sFetch;
sFetch: substate_n = sExecute;
sExecute:
unique casez (IR_r)
`LW: substate_n = sMemory;
default: substate_n = sNewPC;
endcase
sMemory: substate_n = sNewPC;
default: substate_n = sNewPC;
endcase
typedef enum logic [1:0] { sNewPC, sFetch, sExecute, sMemory } state_s;
state_s substate_r, substate_n;
NewPC
Fetch
Execute
Memory
~(LW)
LW
Useful Discipline: Always give a default: for unique casez, even if it is empty.
(This enables pass-thru of settings prior to the casez statement; otherwise synthesizer will assume it’s don’t care. )

## Slide 16: Coding Control: Enables
always_comb
begin
pc_en = 1’b0;
imem_en = 1’b0;
IR_en = 1’b0;
dmem_wen = 1’b0;
dmem_ren = 1’b0;
rf_wen = 1’b0;
unique case (substate_n)
sNewPC:
begin
pc_en = 1’b1;
rf_wen = writes_rf_c;
dmem_wen = writes_dmem_c;
end
sFetch: imem_ren = 1’b1;
sExecute: IR_en = 1’b1;
sMemory: dmem_ren = 1’b1;
default:
endcase
end
NewPC
Fetch
Execute
Memory
pc_en = 1
rf_wen = writes_rf_c;
if (writes_dmem_c)
dmem_wen=1
pc_en = 1
rf_wen=writes_rf_c
imem_ren=1
IR_en=1
dmem_ren=1

## Slide 17
reg writes_rf_c; // aka RegWrite;
always_comb
unique casez (IR_r)
`LW: writes_rf_c = 1’b1;
‘SW: writes_rf_c = 1’b0;
`BNE: writes_rf_c = 1’b0;
`ADDIU: writes_rf_c = 1’b1;
…
default: writes_rf_c = 1’b0;
endcase
reg writes_dmem_c; // aka MemWrite;
always_comb
unique casez (IR_r)
‘SW: writes_dmem_c = 1’b1;
…
default: writes_dmem_c = 1b’0;
endcase
Coding Control: Combinationals
- combinational decode logic often does not require state-sensitivity
reg rf_wr_sel; // aka WriteToReg;
always_comb
unique casez (IR_r)
‘LW: rf_wr_sel = 1’b1;
…
default: rf_wr_sel = 1b’0;
endcase
remaining:
dest_sel
ALUSrc
ALUOp
pc_sel
etc…

## Slide 18: Fixing Critical Paths: Add registers on slow paths and fix state machine logic accordingly.
pc_en
NewPC
Fetch
Execute
Memory
0
1
2
4
IR_en
dmem_ren
dmem_wen
rf_wen
pc_sel
rf_wr_sel
dest_sel
imem_ren
3
RF

## Slide 19: Additional Complexities
NewPC
Fetch
Execute
Memory
reset
PC=0
r0 = 0
etc
Factorial
Init
Factorial
Iterate
Factorial
Cleanup
bootstrapping states
complex
variable-
latency
instruction